## Slide 1: CS 3700 Networks and Distributed Systems
Internet Architecture
(Layer cake and an hourglass)
Revised 1/10/2024

## Slide 2: Organizing Network Functionality
Networks are built from many components
  Networking technologies
    Ethernet, Wifi, Bluetooth, Fiber Optic, Cable Modem, DSL
  Network styles
    Circuit switch, packet switch
    Wired, Wireless, Optical, Satellite
  Applications
    Email, Web, FTP, Bittorrent, Fortnite
How do we make all this stuff work together?!

## Slide 3: Problem Scenario
Web
Email
Signal
Ethernet
802.11
Bluetooth
VC
Cellular
This is a nightmare scenario
Huge amounts of work to add new apps or media
Limits growth and adoption

## Slide 4: More Problems
Signal
Ethernet
802.11
Signal
Application endpoints may not be on the same media

## Slide 5: Solution: Use Indirection
Web
Email
Signal
Ethernet
802.11
Bluetooth
VC
Cellular
Magical Network Abstraction Layer
O(1) work to add new apps, media
Few limits on new technology
API
API
API
API

## Slide 6: Layered Network Stack
Modularity
  Does not specify an implementation
  Instead, tells us how to organize functionality
Encapsulation
  Interfaces define cross-layer interaction
  Layers only rely on those below them
Flexibility
  Reuse of code across the network
  Module implementations may change
Unfortunately, there are tradeoffs
  Interfaces hide information
  As we will see, may hurt performance…
Applications
Physical
Media
Layer N
Layer 1
Layer 2
…
Layer 1.1

## Slide 7: Key Questions
How do we divide functionality into layers?
  Routing
  Congestion control
  Error checking
How do we distribute functionality across devices?
  Example: who is responsible for security?
Switch
Switch
Router
  Security
  Fairness
  And many more…

## Slide 8: Outline
Layering
  The OSI Model
Distribution
  The End-to-End Argument

## Slide 9: The ISO OSI Model
OSI: Open Systems Interconnect Model
Application
Presentation
Session
Transport
Network
Data Link
Physical
Network
Data Link
Application
Presentation
Session
Transport
Network
Data Link
Physical
Host 1
Router
Host 2
Physical
All devices implement the first N layers
Layers communicate peer-to-peer
Layers communicate peer-to-peer

## Slide 10: Layer Features
Service
  What does this layer do?
Interface
  How do you access this layer?
Protocol
  How is this layer implemented?
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 11: Physical Layer
Service
  Move information between two systems connected by a physical link
Interface
  Specifies how to send one bit
Protocol
  Encoding scheme for one bit
  Voltage levels
  Timing of signals
Examples: coaxial cable, fiber optics, radio frequency transmitters
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 12: Data Link Layer
Service
  Data framing: boundaries between packets
  Media access control (MAC)
  Per-hop reliability and flow-control
Interface
  Send one packet between two hosts connected to the same media
Protocol
  Physical addressing (e.g. MAC address)
Examples: Ethernet, Wifi, DOCSIS
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 13: Network Layer
Service
  Deliver packets across the network
  Handle fragmentation/reassembly
  Packet scheduling
  Buffer management
Interface
  Send one packet to a specific destination
Protocol
  Define globally unique addresses
  Maintain routing tables
Example: Internet Protocol (IP), IPv6
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 14: Transport Layer
Service
  Multiplexing/demultiplexing connections
  Congestion control
  Reliable, in-order delivery
Interface
  Send message to a destination’s port
Protocol
  Port numbers
  Reliability/error correction
  Flow-control information
Examples: UDP, TCP
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 15: Session Layer
Service
  Access management
  Synchronization
Interface
  It depends…
Protocol
  Token management
  Insert checkpoints
Examples: none
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 16: Presentation Layer
Service
  Convert data between different representations
  E.g. big endian to little endian
  E.g. ASCII to Unicode
Interface
  It depends…
Protocol
  Define data formats
  Apply transformation rules
Examples: none
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 17: Application Layer
Service
  Whatever you want :)
Interface
  Whatever you want :D
Protocol
  Whatever you want ;)
Examples: turn on your smartphone and look at the list of apps
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 18: Encapsulation
How does data move through the layers?
Application
Presentation
Session
Transport
Network
Data Link
Physical
Data
Data

## Slide 19: Real Life Analogy
Postal Service
Label contains routing info
Un-packing
Doesn’t know contents of letter
Doesn’t know how the Postal network works

## Slide 20: Network Stack in Practice
Application
Presentation
Session
Transport
Network
Data Link
Physical
Network
Data Link
Application
Presentation
Session
Transport
Network
Data Link
Physical
Host 1
Router
Host 2
Physical
Video Client
UDP
Video Server
UDP
FTP Client
TCP
IP
Ethernet
IP
Ethernet
FTP Server
TCP
IP
Ethernet
802.11n
802.11n
802.11n

## Slide 21: Encapsulation, Revisited
Web Server
TCP
IP
Ethernet
HTTP Header
TCP Header
IP Header
Ethernet Header
Ethernet Trailer
Web Page
HTTP Header
Web Page
TCP Header
HTTP Header
Web Page
IP Header
TCP Header
HTTP Header
Web Page
TCP Segment
IP Datagram
Ethernet Frame

## Slide 22: The Hourglass
IPv4
TCP, UDP, ICMP
HTTP, FTP, RTP, IMAP, Jabber, …
Ethernet, 802.11x, DOCSIS, …
Fiber, Coax, Twisted Pair, Radio, …
One Internet layer means all networks interoperate
All applications function on all networks
Room for development above and below IP
But, changing IP is insanely hard
Think about the difficulty of deploying IPv6…

## Slide 23: Orthogonal Planes
Application
Presentation
Session
Transport
IP
Data Link
Physical
Data Plane
BGP
RIP
OSPF
Control Plane
Well cover this later…

## Slide 24: Reality Check
The layered abstraction is very nice
Does it hold in reality?
No.
Firewalls
Analyze application layer headers
Transparent Proxies
Simulate application endpoints within the network
NATs
Break end-to-end network reachability

## Slide 25: Outline
Layering
  The OSI Model
Distribution
  The End-to-End Argument

## Slide 26: Where to Place Functionality
How do we distribute functionality across devices?
  Example: who is responsible for security?
Switch
Switch
Router
?
?
?
?
?
“The End-to-End Arguments in System Design”
  Saltzer, Reed, and Clark
  The Sacred Text of the Internet
  Endlessly debated by researchers and engineers

## Slide 27: Basic Observation
Some applications have end-to-end requirements
  Security, reliability, etc.
Implementing this stuff inside the network is hard
  Every step along the way must be fail-proof
End hosts…
  Can’t depend on the network (recall Kahn’s ground-rules)
  Can satisfy these requirements without network level support

## Slide 28: Example: Reliable File Transfer
Solution 1: Make the network reliable
Solution 2: App level, end-to-end check, retry on failure
Integrity Check
Integrity Check
Integrity Check
App has to do a check anyway!

## Slide 29: Example: Reliable File Transfer
Solution 1: Make the network reliable
Solution 2: App level, end-to-end check, retry on failure
Please Retry
Full functionality can be built at App level
In-network implementation…
  Doesn’t reduce host complexity
  Does increase network complexity
  Increased overhead for apps that don’t need functionality
But, in-network performance may be better

## Slide 30: Another example: Anonymity
Should we implement this in the network?
How about at the endpoints?
?
?
?
?
?

## Slide 31: The End-to-End Argument
“Don’t implement a function at the lower levels of the system unless it can be completely implemented at this level” (Peterson and Davie)
Basically, unless you can completely remove the burden from end hosts, don’t bother

## Slide 32: Differences of Opinion
Don’t implement anything in the network that can be implemented correctly by the hosts
Make network layer absolutely minimal
Ignore performance issues
Think twice before implementing functionality in the network
If hosts can implement functionality correctly, implement it a lower layer only as a performance enhancement
But do so only if it does not impose burden on applications that do not require that functionality
Radical Interpretation
Moderate Interpretation

## Slide 33: Reality Check, Again
Layering and E2E principals regularly violated
Firewalls
Transparent Proxies
NATs
Conflicting interests
  Architectural purity
  Commercial necessity

## Slide 34: Takeaways
Layering is a nice way to organize network functions
Unified Internet layer decouples apps from network hardware, enables innovation
E2E argument (attempts) to keep IP layer simple
Think carefully when adding functionality into the network