## Slide 1: CS 4700 Networks and Distributed Systems
Crash Course in C Sockets
(Prepare yourself for Project 1)
Revised 8/19/15

## Slide 2: Socket Programming
Goal: familiarize yourself with socket programming
  Why am I presenting C sockets?
  Because C sockets are the de-facto standard for networking APIs
Project 1: Implement a semi-trivial protocol
  We will have a server set up for you
  There may be chances for extra credit ;)

## Slide 3: C Sockets
Socket API since 1983
  Berkeley Sockets
  BSD Sockets (debuted with BSD 4.2)
  Unix Sockets (originally included with AT&T Unix)
  Posix Sockets (slight modifications)
Original interface of TCP/IP
  All other socket APIs based on C sockets

## Slide 4: Outline
High-level Design
Server API
Client API + Name resolution
Other Considerations

## Slide 5: Clients and Servers
A fundamental problem: rendezvous
  One or more parties want to provide a service
  One or more parties want to use the service
  How do you get them together?
Solution: client-server architecture
  Client: initiator of communication
  Server: responder
  At least one side has to wait for the other
    Service provider (server) sits and waits
    Clients locates servers, initiates contact
    Use well-known semantic names for location (DNS)

## Slide 6: Key Differences
Execute on-demand
Unprivileged
Simple
(Usually) sequential
Not performance sensitive
Always-on
Privileged
Complex
(Massively) concurrent
High performance
Scalable
Clients
Servers

## Slide 7: Similarities
Share common protocols
  Application layer
  Transport layer
  Network layer
Both rely on APIs for network access

## Slide 8: Sockets
Basic network abstraction: the socket
Socket: an object that allows reading/writing from a network interface
In Unix, sockets are just file descriptors
  read() and write() both work on sockets
  Caution: socket calls are blocking

## Slide 9: C Socket API Overview
Clients
gethostbyname()
socket()
connect()
write() / send()
read() / recv()
close()
Servers
socket()
bind()
listen()
while (whatever) {
accept()
read() / recv()
write() / send()
close()
}
close()

## Slide 10: int socket(int, int, int)
Most basic call, used by clients and servers
Get a new socket
Parameters
  int domain: a constant, usually PF_INET
  int type: a constant, usually SOCK_STREAM or SOCK_DGRAM
    SOCK_STREAM means TCP
    SOCK_DGRAM means UDP
  int protocol: usually 0 (zero)
Return: new file descriptor, -1 on error
Many other constants are available
  Why so many options?
The C socket API is extensible.
The Internet isn’t the only network domain
TCP/UDP aren’t the only transport protocols
In theory, transport protocols may have different dialects

## Slide 11: int bind(int, struct sockaddr *, int)
Used by servers to associate a socket to a network interface and a port
  Why is this necessary?
Parameters:
  int sockfd: an unbound socket
  struct sockaddr * my_addr: the desired IP address and port
  int addrlen: sizeof(struct sockaddr)
Return: 0 on success, -1 on failure
  Why might bind() fail?
Each machine may have multiple network interfaces
  Example: Wifi and Ethernet in your laptop
  Example: Cellular and Bluetooth in your phone
Each network interface has its own IP address
We’ll talk about ports next…

## Slide 12: Port Numbers
Basic mechanism for multiplexing applications per host
  65,535 ports available
  Why?
Ports <1024 are reserved
  Only privileged processes (e.g. superuser) may access
  Why?
  Does this cause security issues?
“I tried to open a port and got an error”
  Port collision: only one app per port per host
  Dangling sockets…
TCP/UDP port field is 16-bits wide
In olden times, all important apps used low port numbers
Examples: IMAP, POP, HTTP, SSH, FTP
This rule is no longer useful

## Slide 13: Dangling Sockets
Common error: bind fails with “already in use” error
OS kernel keeps sockets alive in memory after close()
  Usually a one minute timeout
  Why?
Allowing socket reuse
int yes=1;
if (setsockopt(listener, SOL_SOCKET, SO_REUSEADDR, &yes, sizeof(int)) == -1) { perror("setsockopt");
exit(1);
}
Closing a TCP socket is a multi-step process
Involves contacting the remote machine
“Hey, this connection is closing”
Remote machine must acknowledge the closing
All this book keeping takes time

## Slide 14: struct sockaddr
Structure for storing naming information
  But, different networks have different naming conventions
  Example: IPv4 (32-bit addresses) vs. IPv6 (64-bit addresses)
In practice, use more specific structure implementation
struct sockaddr_in my_addr;
memset(&my_addr, 0, sizeof(sockaddr_in));
my_addr.sin_family = htons(AF_INET);
my_addr.sin_port = htons(MyAwesomePort);
my_addr.sin_addr.s_addr = inet_addr("10.12.110.57");

## Slide 15: htons(), htonl(), ntohs(), ntohl()
Little Endian vs. Big Endian
  Not a big deal as long as data stays local
  What about when hosts communicate over networks?
Network byte order
  Standardized to Big Endian
  Be careful: x86 is Little Endian
Functions for converting host order to network order
  h to n s – host to network short (16 bits)
  h to n l – host to network long (32 bits)
  n to h * – the opposite

## Slide 16: Binding Shortcuts
If you don’t care about the port
  my_addr.sin_port = htons(0);
  Chooses a free port at random
  This is rarely the behavior you want for a server (but okay for clients)
If you don’t care about the IP address
  my_addr.sin_addr.s_addr = htonl(INADDR_ANY);
  INADDR_ANY == 0
  Meaning: don’t bind to a specific IP
  Traffic on any interface will reach the server
    Assuming it’s on the right port
  This is usually the behavior you want for a server (but not clients)

## Slide 17: int listen(int, int)
Put a socket into listen mode
  Used on the server side
  Wait around for a client to connect()
Parameters
  int sockfd: the socket
  int backlog: length of the pending connection queue
    New connections wait around until you accept() them
    Just set this to a semi-large number, e.g. 1000
Return: 0 on success, -1 on error

## Slide 18: int accept(int, void *, int *)
Accept an incoming connection on a socket
Parameters
  int sockfd: the listen()ing socket
  void * addr: pointer to an empty struct sockaddr
    Clients IP address and port number go here
    In practice, use a struct sockaddr_in
  int * addrlen: length of the data in addr
    In practice, addrlen == sizeof(struct sockaddr_in)
Return: a new socket for the client, or -1 on error
  Why?
You don’t want to consume your listen() socket
Otherwise, how would you serve more clients?
Closing a client connection shouldn’t close the server

## Slide 19: close(int sockfd)
Close a socket
  No more sending or receiving
shutdown(int sockfd, int how)
  Partially close a socket
    how = 0; // no more receiving
    how = 1; // no more sending
    how = 2; // just like close()
  Note: shutdown() does not free the file descriptor
  Still need to close() to free the file descriptor

## Slide 20: C Socket API Overview
Clients
gethostbyname()
socket()
connect()
write() / send()
read() / recv()
close()
Servers
socket()
bind()
listen()
while (whatever) {
accept()
read() / recv()
write() / send()
close()
}
close()

## Slide 21: struct * gethostbyname(char *)
Returns information about a given host
Parameters
  const char * name: the domain name or IP address of a host
  Examples: “www.google.com”, “10.137.4.61”
Return: pointer to a hostent structure, 0 on failure
  Various fields, most of which aren’t important
struct hostent * h = gethostname(“www.google.com”);
struct sockaddr_in my_addr;
memcpy(&my_addr.sin_addr.s_addr, h->h_addr,
h->h_length);

## Slide 22: int connect(int, struct sockaddr *, int)
Connect a client socket to a listen()ing server socket
Parameters
  int sockfd: the client socket
  struct sockaddr * serv_addr: address and port of the server
  int addrlen: length of the sockaddr structure
Return: 0 on success, -1 on failure
Notice that we don’t bind() the client socket
  Why?

## Slide 23: write() and send()
ssize_t write(int fd, const void *buf, size_t count);
  fd: file descriptor (ie. your socket)
  buf: the buffer of data to send
  count: number of bytes in buf
  Return: number of bytes actually written
int send(int sockfd, const void *msg, int len, int flags);
  First three, same as above
  flags: additional options, usually 0
  Return: number of bytes actually written
Do not assume that count / len == the return value!
  Why might this happen?

## Slide 24: read() and recv()
ssize_t read(int fd, void *buf, size_t count);
  Fairly obvious what this does
int recv(int sockfd, void *buf, int len, unsigned int flags);
  Seeing a pattern yet?
Return values:
  -1: there was an error reading from the socket
    Usually unrecoverable. close() the socket and move on
  >0: number of bytes received
    May be less than count / len
  0: the sender has closed the socket

## Slide 25: More Resources
Beej’s famous socket tutorial
  http://beej.us/net2/html/syscalls.html